Towards Deterministic Rounding Behaviour in Quantized Convolutions
(A design-note-in-progress) 9-Nov-2018
Greg Smith smithg@qti.qualcomm.com
# Introduction
This document discusses the specification of our 8-bit and 16-bit quantization mechanism, and proposes a minor adjustment which will support, under a reasonable set of conditions, bit-reproducible rounding in convolution operations (i.e. exactly the same results can be reproduced by an independent implementation). This can be useful when network designers wish to include compensation for run-time rounding errors as part of network training, and thus need to model those errors exactly.
To illustrate, consider an 8x8→8 convolution with 32-bit biases, for the case where the output quantization range is predetermined (and weights and biases are pre-quantized).
This operation can be broken down as these steps:
- A convolution, processed as integer operations on the quantized inputs
- Addition of bias values; the scaling of these depends on quantization
- An offset, scaling, saturation operation which generates the final output. The scaling and offset are functions of the input and output scaling, and the operation itself can be expressed in simple integer calculation (add, multiply, right-shift, saturate).
A goal of this document is to develop a recommendation which allows the result of the process to be reproducible exactly in another implementation, provided:
- The quantization ranges of the input, output, and weights comply with the recommendations below (and, of course, match exactly across the two implementations);
- The 32-bit bias values are encoding using a quantization step which matches in_step * weight_step * k (calculated as a floating point result) where in_step and weight_step are the quantization steps of those inputs, and k is a power of 2. This allows the scaling of the bias values to the operation to be reproducible [This needs more work].
- The calculation and use of the scaling and offset values, for the convolution output, are done as described below [yet to be added].

# Terms
- Floating point or float refers to 32-bit IEEE floating point.
- Lossless refers to a computation done without no rounding, so that the actual result is the same as the mathematically exact result. Integer multiply and adds are lossless. Floating point overflow/underflow, and integer overflow, are not considered, and assumed not to occur by design.
- Reproducible describes a computation which may have rounding errors, but from which we can expect two implementations to produce identical results, provided the sequence of such operations is adequately specified.
# Quantization Overview
When storing “Quantized” data we use a finite number ( e.g. 2^8 or 2^16 ) of integer codes to represent continuous data; for a given set quantized values q_i , we need to known the quantization parameters in order to convert these to the 'dequantized' values x_i they represent.
This is a simple linear relationship, and we have two ways to represent it:

Scale and zero s, z:
x_i ~=~ s (q_i-z)	(1)

Nominal min and max %alpha, %beta :
x_i ~=~ %alpha + {%beta-%alpha} over N q_i	(2)

Here, %alpha is simply the dequantized value associated with quantized value q_i=0 , and %beta is the value associated with q_i=N ; for 8-bit data we use N=255, so that %alpha, %beta represent the smallest and largest possible x.
Conversions between the two forms may be made as follows:
s~=~ {%beta-%alpha} over N; ~ z ~=~ - {%alpha over s}	(3)

%alpha ~=~ -zs; ~ %beta ~=~ (N-z)s	(4)

For reasons of computational convenience, we always require:
s > 0;~ z in setZ ;~ 0 <= z <= N	(5)

… which together imply: %alpha <= 0 <= %beta;~ %alpha < %beta
i.e. the range may not be empty, and must include zero.

# Lossless Conversion Between Representations
It is possible to restrict the allowed quantization parameters, in such a way as to guarantee that the computations in (3)and (4) are lossless when performed in floating point.
## 8-bit Quantization, N=255:
By choosing a value of s which can be expressed in at most 16 mantissa bits ( i.e. it can be expressed exactly as s=k 2^e where k,e in setZ , 32768 <= k <= 65535 ) the operations in (4) are lossless when done in single-precision floats, and the resulting %alpha, %beta are such that %beta-%alpha is lossless and yields exactly 255 s; thus the formulae for s and z in (3) will give the original value exactly (see section 7 regarding division by 255).
Also, with these constraints, it is possible to losslessly convert quantized data to float: either x_i `=` s ( q_i -z ) or x_i `=`%alpha + sq_i may be used, and the conversion will be exact if done in IEEE floats.
Conversion from float to quant is lossy, of course; it may be useful to define a reproducible method based on a given quantization specification, but currently I don’t have one and it may not be trivial to bring the existing code to comply to a given specification – values which fall nearly or exactly halfway between two quantization levels are at risk of being quantized differently in different implementations. Furthermore, the process of finding a quantization spec to cover a given range of floats is not as yet defined in a reproducible form.
## 16-bit Quantization
For the 16-bit case, it’s possible to use N`=`2^16-1`=`65535 , but in order to get the exact computations we would need to generate min/max values which are representable in floats as differing by exact multiples of 65535, which is a problematic constraint when only 24 mantissa bits are available.
Instead we use N`=`2^16`=`65536 , and continue to use (3) and (4) ; this means that %alpha is still the minimum representable value (code 0) but %beta is the ‘nominal’ maximum: the value which would be represented by code 65536.
If we choose values of s which are representable in 22 mantissa bits, the multiplications in (4) to find %alpha, %beta are generally not lossless, but if floating point operations are done with convergent rounding (the default mode) the difference %beta-%alpha in (3) will always[1] give exactly 65536 s ; the multiplication by (1/N) is lossless and thus we can recover s exactly. The value of z found as z=-%alpha/s can be inexact, but the worst absolute error is about +- 2^-8 so z can be easily corrected by rounding to the nearest integer.
[1] I don't have a proof for this, but testing over all 2^37 cases (all cases with a specific s exponent) found no failures.
Dequantization of 16-bit floats should be done as x_i = s ( q_i – z ) where the subtraction is an exact integer operation, the difference is converted losslessly to float, and the multiplication by s is lossy but reproducible.

# Determining Quantization For a Given Range of Data
## 8-bit Quantization, N=255
Whenever we need to quantize a given range of floating point values lbrace x_i rbrace , the following process is recommended to find the quantization parameters:
Find the actual range over lbrace x_i rbrace , including zero:
x_min ~=~ min lbrace 0 ,` x_0,` x_1,` … rbrace
x_max ~=~ max lbrace 0 ,` x_0,` x_1,` … rbrace
- In the case where x_min = 0 :
  - set z = 0, and s` =` x_max /255
  - If x_max=0 , all of the x_i are zero and we can use an arbitrary value such as s=2^-8
- Otherwise if x_max=0 :
  - set z = 255, and s` =` -x_min /255
- Otherwise we need to find an integer zero point in 1...254, and scale which encompass the desired range. This method finds the smallest feasible s:
  - Find approximate value for the zero point, hat z ~=~ -{ 255 cdot x_min }over { x_max - x_min } in range [0,255]
  - Two candidate z values are the nearest integers z_0 `=` lfloor hat z rfloor, ~ z_1 `=` z_0+1
  - Corresponding minimal s values are s_0~=~ -x_min over z_0 , ~ s_1 ~=~ x_max over {255-z_1} ;
  - use (s,`z) `=` (s_0,`z_0) if z_0 > 0 and ( z_1 >=255 or s_0 < s_1 ), otherwise use (s,`z) `=` (s_1,`z_1)
- In any case round the s value upward, if needed, to the next value which may be expressed in 16 mantissa bits.
- %alpha, %beta can be then found via (4); and it is guaranteed that the conditions in (5) are met, and that %alpha <= x_min, ` x_max <= %beta ; no solution with a smaller s exists.

Note that the condition s_0 < s_1 can be evaluated as (z_0-254)x_min `<` z_0 x_max

This procedure can be used to “correct” a possibly unreliable (%alpha, %beta) range to a similar one which meets the critera: if the (x_min, x_max) are set to the given (%alpha, %beta) , the new (%alpha, %beta) resulting will include the original range; and should be identical to the original range when that already meets the criteria (i.e. the process is idempotent).

However, the procedure is not considered to reproducible for arbitrary (x_min, x_max) ; in some cases, slight differences in the way the computation is done could produce different choice of z, for instance, when the s_0,s_1 are very similar or identical.

Examples:
(x_min,`x_max) = (0,`1) ~drarrow~ (s,`z) = (0.003921628,`0) ~drarrow~ (%alpha,`%beta)=(0,`1.0000151)
Here, s = "0x8081" times 2^-23 and %beta = "0x80007F" times 2^-23 exactly.

(x_min,`x_max) = (-1,`1) ~drarrow~ (s,`z) = (0.0078742504,`128) ~drarrow~ (%alpha,`%beta)=(-1.0079041,`1.0000298)
Here, s = "0x8103" times 2^-22 and %alpha = -"0x8103" times 2^-15 ,` %beta = "0x40007D" times 2^-22 exactly. It's also possible to use the same value of s, and z=127.

## 16-bit Quantization, N=65536
The method for finding scaling over a given range is below. This assumes that we don’t want x_max to map to at most code 65535; we don't want it to map to 65536 and then be truncated to 65535. So we want a quantization specification for which %alpha <= x_min, ` x_max <= (%beta-s) .
Find the actual range over lbrace x_i rbrace , including zero:
x_min ~=~ min lbrace 0 ,` x_0,` x_1,` … rbrace
x_max ~=~ max lbrace 0 ,` x_0,` x_1,` … rbrace
- In the case where x_min = 0 :
  - set z = 0, and s` =` x_max /65535
  - If x_max=0 , all of the x_i are zero and we can use an arbitrary value such as s=2^-16
- Otherwise if x_max=0 :
  - set z = 65535, and s` =` -x_min /65535
- Otherwise we need to find an integer zero point in 1..65534, and scale which encompass the desired range. This method finds the smallest s:
  - Find approximate value for the zero point, hat z ~=~ -{65535 cdot x_min }over { x_max - x_min } ( in range [0,65535])
  - Two candidate z values are the nearest integers z_0 `=` lfloor hat z rfloor, ~ z_1 `=` z_0+1
  - Corresponding minimal s values are s_0~=~ -x_min over z_0 , ~ s_1 ~=~ x_max over {65535-z_1} ;
  - use (s,`z) `=` (s_0,`z_0) if z_0 > 0 and ( z_1 >=65535 or s_0 < s_1 ), otherwise use (s,`z) `=` (s_1,`z_1)
- In any case round the s value upward, if needed, to the next value which may be expressed in 22 mantissa bits.
- %alpha, %beta can be then found via (4); and it is guaranteed that the conditions in (5) are met, and that %alpha <= x_min, ` x_max <= (%beta-s) ; no solution with a smaller s exists.

The condition s_0 < s_1 can be evaluated as (z_0-65534)x_min `<` z_0 x_max
For the 8-bit case it is possible to have %alpha < 0, `%beta=0 ; but for the 16-bit case z <=65535, so %beta >=s

Unlike the N=255 process, this is not idempotent – if resulting (%alpha,%beta) are used as (x_min, x_max) and the process is run again, the new range will be larger.
Thus it should only be used to find a “new” nominal range to cover a given range of values, not to ‘correct’ existing nominal ranges.
Correcting an existing nominal range (i.e. modifying it as little as possible to meet conditions in (5), and the constraint on s ) can be done by the following idempotent method:
- find s,z using (3);
- round z to the nearest integer, limiting it to range 0..65535
- round s to the nearest value which can be expressed in 22 mantissa bits.
- Convert back to (%alpha,%beta) using (4)
Applying this correction to an arbitrary (%alpha,%beta) range may produce only a small change in the interpretation of the quantized codes; mostly due to the rounding of z, which produces an offset of at most +- 2^-17 (%beta-%alpha) .
In the special case where %alpha=0 , the correction can be done by simply rounding %beta to the nearest value which can be expressed in 22 mantissa bits, since in this case z=0 and %beta=2^16 s
Examples:
(x_min,`x_max) = (0,`1) ~drarrow~ (s,`z) = (1.5259029 times 10^-5 ,`0) ~drarrow~ (%alpha,`%beta)=(0,`1.0000157)
Here, s = "0x200021" times 2^-37 and %beta = "0x200021" times 2^-21 exactly.

(x_min,`x_max) = (-1,`1) ~drarrow~ (s,`z) = (3.0518524 times 10^-5 ,`32768) ~drarrow~ (%alpha,`%beta)=(-1.0000305,`1.0000305)
Here, s = "0x200041" times 2^-36 and %alpha , %beta = -+ "0x200041" times 2^-21 exactly.

# Final Rounding in Convolutions
For a convolution, or a matrix multiply, we want to find
{ bold "y" } ~=~ { bold "x" } * { bold "w" }`+` { bold "b" }
where the input values are actually represented by quantized values { bold hat "x" },{ bold hat "w" },{ bold hat "b" } , defined by quantization parameters
{ bold "w" }~=~ s_w ({ bold hat "w" }-z_w) { bold "b" }~=~ s_b ({ bold hat "b" }-z_b)
...and we want the output as { bold hat "y" } such that { bold "y" }~=~ s_y ({ bold hat "y" }-z_y) . All of the s_"*" and z_"*" are given.
(the details of the convolution subscripts and summation are omitted, since the discussion applies to any sum-of-products operation).
Also, for now this discussion applies only to operations with 8-bit inputs and outputs.
First, we will find a integer convolution result as follows:
{ bold hat "p" } ~=~ ( {bold hat "x" } - z_x ) * ( {bold hat "w" } - z_w )
This is a lossless integer operation, and it is clear that
{ bold "y" } ~=~ s_x s_w {bold hat "p"}`+` { bold "b" } newline ~drarrow~ { bold hat "y" } - z_y ~=~ {s_x s_w} over s_y {bold hat "p"}`+` { 1 over s_y}{ bold "b" } newline ~drarrow { bold hat "y" } - z_y ~=~ {s_x s_w} over s_y left ( {bold hat "p"} ~+~ {1 over {s_x s_w} }{ bold b } right ) newline ~drarrow { bold hat "y" } ~=~ {s_x s_w} over {%lambda s_y }left ( %lambda {bold hat "p"} ~+~ {{%lambda s_b} over {s_x s_w} }( { hat bold b } - z_b ) ~+~ { %lambda s_y} over { s_x s_w } z_y right )
(where %lambda is a scaling constant to be discussed below)
So the rest of the computation consists of:
- Scaling the bias: i.e. finding {bold hat "b"}_p ~=~ {{%lambda s_b} over {s_x s_w }} ( {bold hat "b"} - z_b ) , rounding to nearest integer;
- Finding the output offset, Z_p ~= { {%lambda s_y} over {s_x s_w }} z_y , and rounding it to the nearest integer
- Finding the overall scale S_p ~= { {s_x s_w } over { %lambda s_y}} in some fixed-point format.
- The result is then { bold hat "y" } ~=~ S_p left ( %lambda { bold hat "p" } ~+~ { bold hat "b" }_p ~+~ Z_p right)
%lambda is chosen as a power of 2, and is usually 1; so the multiplication by %lambda is actually a shift.
In most cases, S_p is considerably less than zero even when %lambda=1 , so the process of rounding Z_p ~= { 1 over {S_p }} z_y and { bold hat "b" }_p to integer produces rounding errors which are small relative to the final rounding. In situations where this is not true, it may be necessary to use a larger %lambda value to obtain a smaller S_p , thus diminishing the visibility of those rounding errors.
In order for this to be reproducible, we need to define the following in a way which makes them reproducible:
- How %lambda is chosen;
- How S_p is calculated and rounded;
- How {bold hat "b"}_p , ` Z_p are calculated and rounded; and
- How the multiplication by S_p is to be done.
[note – currently we support a %lambda in some of the convolutions, but it can't be used to control rounding errors as above since it's applied to the full sum, not just the p term. It is used only to ensure S_p < 1 ]
… In progress....
The multiplication by S_p is done by finding the full 64-bit product of the fixed-bit S_p value and the final sum; adding a rounding bias of 2^30 , and then shifting the result right 31 bits. The result is saturated so as not to exceed the range 0...255.
# Note: Division by 255 in floats
If a,b are floating-point values such that the float product p=255 cdot b is lossless, and a=p, then the floating-division a/(float)255.0 will yield exactly b, we rely on this to have exact conversion from (%alpha,%beta) to s in the 8-bit case.
If we choose instead to find a*(float)(1./255.0), to reduce computation time, the exact result is not guaranteed, since (1/255.0) falls about midway between two representable values. The nearest float representation of (1/255.0) is too large by 2.319 times 10^-10 ; so if it happens that the multiplication rounds upwards, the result can be inexact even though an exact quotient is representable. This can be avoided by doing the calculation as b = r_0 a `+` r_1 a , where r_0 = 3.921568859 times 10^-3 , r_1 = -2.3191758 times 10^-10 ; the operation should be done using a ‘fused multiply-add’ so the larger product is not fully rounded before the smaller is added.